## Slide 1: Uncertainty Quantification and Global Sensitivity Analysis Methods for Monte Carlo Radiation Transport Solvers
Dissertation Presentation
Kayla Clements
Advisor: Dr. Todd Palmer
School of Nuclear Science and Engineering
December 10, 2024
Notes: Reminders from TP:
As you think about your slides, I recommend illustrating concepts with simple examples, if possible, and skipping details of derivations.
Being able to convince your committee that what you plan to do is a) new, and b) needed is an important part of the proposal/presentation. I typically want to see some evidence when I am being persuaded, and that’s where familiarity with previous research is important.

## Slide 2: Bottom Line Up Front
Zoom out: what are we talking about?
Variance deconvolution is a novel method for uncertainty quantification (UQ) and global sensitivity analysis (GSA) when the underlying solver is stochastic that does not require resolving the stochastic solver variance to near-zero.
Variance deconvolution is a non-intrusive approach that can be paired with any stochastic solver and was tested with multiple Monte Carlo radiation transport codes.
Variance deconvolution was shown theoretically and numerically to accurately compute key UQ and GSA statistics for a lower computational cost than the standard approach.
This work has been published in the Journal of Quantitative Spectroscopy and Radiative Transfer and has been presented at academic conferences such as the International Conference on Mathematics and Computational Methods Applied to Nuclear Science and Engineering (aka M&C) and the annual conferences of the American Nuclear Society and the Society of Industrial and Applied Mathematics.

## Slide 3: Context

## Slide 4: What is a computational model?
Computational modeling diagram[1].
Data
Model
Simulation
Test simulation
?

## Slide 5: Deterministic vs Stochastic Methods
Deterministic
Directly solves equation or system of equations
Computer codes use numerical methods
Stochastic
Models system as a random process
Computer codes use (pseudo-)random number generators

## Slide 6: Stochastic Method: Monte Carlo Radiation Transport
Monte Carlo Radiation Transport
Initialize particle
Sample distance to next collision
Stream particle – boundary? collision?
Continue until particle is has interaction or exits system
Start again with a new particle until all particles have finished
Repeat for all histories, recording tallies for quantities of interest
x=0
x=L
Streaming Particle
Quantities of interest
Notes: - speaking of monte carlo, pivot to MC rad transport
- this is a very simple rad transport system with some particles streaming
As palmer said, deterministic solve continuous across entire phase space
MC treats physical system as statistical process
- nuclear data for probability distributions
- look at transport algorithm as sampling approach, sampling distributions to tally particle behavior, avg QoI
- variance function of method
- introduce some stochasticity *click*
- want to perform UQ to understand effect, sampling approach
*click*
- however, we know any variance at the end is a result of the solver AND the parameter
- novelty of method is ability to deconvolve w/ tallies that already exist
Pivoting a little bit here, we’ll look at some background for Monte Carlo radiation transport that is I’m sure redundant for many of you. Monte Carlo transport can be used to solve for a QoI as an alternate to deterministic methods, which would explicitly solve a system like this and, for example, get a solution of flux across the entire phase space. Instead, MC methods treat the physical system as a statistical process, using nuclear data to construct probability distributions that describe the various ways particles could behave in the system. Individual particles are simulated and their behavior, like colliding with other particles, exiting the system, etc., is recorded in tallies based on what information the user might want. The central limit theorem can then be applied to extrapolate the tallied behavior of the simulated particles to the average behavior of all particles in the system, with some associated uncertainty based on the number of particles simulated.
This can also be thought of as a sampling approach – you run a certain number of histories and end up with a tally response for each, and you can calculate the mean and variance of your response. The variance you would see here would be a function of the method itself, where increasing the number of histories would decrease the variance.
What if we introduce some stochasticity to our monte carlo problem, for example some uncertainty in the total cross section? *click* We can perform UQ to understand the uncertainty of this parameter propagates throughout the solution by following a sampling UQ approach, which might look something like this *click* where we’ve nested the monte carlo transport solver into the monte carlo for UQ. Ideally, the UQ analysis that we perform for the variance would give the variance of our solution as a function of a UQ parameter. However, we know our QoI is already uncertain as a function of the solver itself; simply computing the variance of our realizations would give over-estimate the variance in a UQ sense, because the solver is adding additional stochasticity. The novelty of the method I’ll introduce now is that it’s able to deconvolve the parameter and solver uncertainties in the solution, and does so using information that a monte carlo transport solver would already tally.
You mentioned here that Monte Carlo is an algorithm rather than a set of equations. This is a bit contentious--some claim that Monte Carlo is nothing more than solving the equations in a different way. Personally, I think show how Monte Carlo solves the equations, but that, really, it's an algorithm for simulating phenomena. Nonetheless, if you make that statement, "them's fighin' words," such that I'd suggest not saying that so that you don't potentially pick a fight you don't want and distract your viewers.

## Slide 7: Uncertainty Quantification (UQ)
Forward uncertainty propagation in computational models[2].
Uncertainty propagation and analysis
Assume accurate model (i.e., no more model parameter tuning).
Uncertainty in system parameters, source terms, systems conditions (initial/boundary).
Propagate uncertainty through model by performing simulations.
Necessary for predictive simulation, robust design, and failure analysis.
Characterize response as function of uncertain parameter(s).

## Slide 8: Global Sensitivity Analysis (GSA)
Uncertainty propagation
Uncertainty analysis
Global sensitivity analysis
Multiple sources of uncertainty
Quantify uncertainty caused by each uncertain parameter.
Understand parameter interactions.
Improve model robustness and reliability.
Prioritize uncertainty reduction.
Rank parameters in order of importance using sensitivity indices.

## Slide 9: Sampling-based methods
Uncertain parameters repeatedly sampled and used as model input
UQ and GSA statistics directly computed from model outputs
Make no assumptions about linearity, smoothness, or regularity of underlying computational model
Can be used as coefficients for surrogates/expansions.
Primary drawback: evaluation cost of multiple code evaluations

## Slide 10: Sampling-based methods

## Slide 11: Background – Sampling uncertainty quantification
Sampling UQ algorithm:
  Sample UQ parameter
  Solve for QoI with existing solver
  Repeat for UQ samples
  Use sampling-based estimators for statistics
Quantity of interest (QoI):
Characterize with
  Mean,
  Variance,
Notes: - an intro to uncertainty quantification
In general, quantity of interest Q, a function of uncertain parameter xi
UQ propagates some source of uncertainty through a numerical code to evaluate statistics
Statistics one might be interested in, using the moment equation. Mean is first moment; variance
You can use a variety of strategies, surrogate and sampling and hybrid
sampling aka MC good for noisy QoI, example alg
In general you have some quantity of interest (or QoI) Q as a result of a numerical code. Uncertainty quantification is the process of propagating some sources of uncertainty through the numerical code to evaluate the statistics of your QoI. Q is then a function of you uncertainty parameter, xi
We have an example here of some statistics of your QoI you might be interested in, as functions of the moment equation. So eq. 1 is the order-p moment equation of Q. Eq 2 is the first moment of Q, aka the expectation or mean. The variance can be taken to be the second moment minus the square of the first moment. A simple example of a stochastic system might look mathematically is eq. 4, where you have some differential equation describing your system, and the parameter xi represents uncertainty in your system.
There are a variety of UQ strategies – surrogates, sampling-based methods, or hybrids of the two. In general, sampling methods (aka MC methods) are good for systems with noisy quantities of interest. Applied to eq. 4, If you have a numerical solver for a solution of y, a sampling UQ approach would be to sample xi and solve for y as a function of it, then do that a number of times (this is referred to as Monte Carlo UQ). Then, calculate your statistics information to understand how your QoI reacts as a function of this uncertain parameter, and we can compare to an exact solution to understand how accurate our sampling approach is.

## Slide 12: Problem Statement
UQ and GSA methods generally assume that the underlying computational model is deterministic – all output variance is from input parameters (parametric).
Stochastic computational models have inherent uncertainty (solver).
Total observed output variance is a combination of parametric variance and solver variance.
Standard approach: increase number of stochastic solver samples, exacerbating high computational cost.
How can we perform efficient sampling-based UQ and GSA on stochastic computational models?

## Slide 13: Existing approaches
MC RT variance will approach zero at the limit of infinite particle histories [23, 113].
Total Monte Carlo and fastTMC [53, 93]
SAMPLER in SCALE [7] and MCNP-pstudy in MCNP[5]
It would be useful to explicitly compute how much the MC RT variance contributes to the total observed variance when the problem contains uncertain parameters [27, 93, 40, 84, 88]
Fix random seed and explicitly treat covariance of now-correlated input parameters [53, 47, 21].
Analyze parametric statistics as functions of solver uncertainty [39, 52].
Emulate stochastic solver as surrogate model and compute statistics of deterministic surrogate model [115, 47, 67, 6, 2, 115].

## Slide 14: Variance deconvolution
(Olson [73] and Geraci) Introduced form variance deconvolution and embedded variance deconvolution
Explicitly computes solver variance within simulation then removes from total observed variance after simulation.
Can be used with any stochastic solver.
Non-intrusive, i.e., does not require modifying underlying computational model, though the model can be slightly modified for improvement in computation time

## Slide 15: Research objectives
Uncertainty quantification (UQ)
  Develop robust theory for an accurate, efficient, and broadly applicable variance deconvolution estimator for uncertainty quantification with stochastic solvers.
Global sensitivity analysis (GSA)
  Assess the effect of stochastic solvers on GSA sensitivity indices.
  Extend UQ framework to develop robust theory for a variance deconvolution estimator for sampling-based sensitivity indices.
Real-world Monte Carlo (MC) radiation transport (RT) problem
  Demonstrate applicability and impact of variance deconvolution on large-scale radiation transport simulations.
  Focus on problems relevant to the Center for Exascale Monte Carlo Neutron Transport (CEMeNT).

## Slide 16: Okay gang, it’s math time

## Slide 17: Background – Sampling uncertainty quantification
Sampling UQ algorithm:
  Sample UQ parameter
  Solve for QoI with existing solver
  Repeat for UQ samples
  Use sampling-based estimators for statistics
Quantity of interest (QoI):
Characterize with
  Mean,
  Variance,
Notes: - an intro to uncertainty quantification
In general, quantity of interest Q, a function of uncertain parameter xi
UQ propagates some source of uncertainty through a numerical code to evaluate statistics
Statistics one might be interested in, using the moment equation. Mean is first moment; variance
You can use a variety of strategies, surrogate and sampling and hybrid
sampling aka MC good for noisy QoI, example alg
In general you have some quantity of interest (or QoI) Q as a result of a numerical code. Uncertainty quantification is the process of propagating some sources of uncertainty through the numerical code to evaluate the statistics of your QoI. Q is then a function of you uncertainty parameter, xi
We have an example here of some statistics of your QoI you might be interested in, as functions of the moment equation. So eq. 1 is the order-p moment equation of Q. Eq 2 is the first moment of Q, aka the expectation or mean. The variance can be taken to be the second moment minus the square of the first moment. A simple example of a stochastic system might look mathematically is eq. 4, where you have some differential equation describing your system, and the parameter xi represents uncertainty in your system.
There are a variety of UQ strategies – surrogates, sampling-based methods, or hybrids of the two. In general, sampling methods (aka MC methods) are good for systems with noisy quantities of interest. Applied to eq. 4, If you have a numerical solver for a solution of y, a sampling UQ approach would be to sample xi and solve for y as a function of it, then do that a number of times (this is referred to as Monte Carlo UQ). Then, calculate your statistics information to understand how your QoI reacts as a function of this uncertain parameter, and we can compare to an exact solution to understand how accurate our sampling approach is.

## Slide 18: Background – Stochastic solvers
Solver uncertainty
Solver tally
Approximate
Example: Monte Carlo Radiation Transport
goal quantity (flux, energy dep., etc)
Solver tally single history’s tally
number of particle histories
Notes: - an intro to uncertainty quantification
In general, quantity of interest Q, a function of uncertain parameter xi
UQ propagates some source of uncertainty through a numerical code to evaluate statistics
Statistics one might be interested in, using the moment equation. Mean is first moment; variance
You can use a variety of strategies, surrogate and sampling and hybrid
sampling aka MC good for noisy QoI, example alg
In general you have some quantity of interest (or QoI) Q as a result of a numerical code. Uncertainty quantification is the process of propagating some sources of uncertainty through the numerical code to evaluate the statistics of your QoI. Q is then a function of you uncertainty parameter, xi
We have an example here of some statistics of your QoI you might be interested in, as functions of the moment equation. So eq. 1 is the order-p moment equation of Q. Eq 2 is the first moment of Q, aka the expectation or mean. The variance can be taken to be the second moment minus the square of the first moment. A simple example of a stochastic system might look mathematically is eq. 4, where you have some differential equation describing your system, and the parameter xi represents uncertainty in your system.
There are a variety of UQ strategies – surrogates, sampling-based methods, or hybrids of the two. In general, sampling methods (aka MC methods) are good for systems with noisy quantities of interest. Applied to eq. 4, If you have a numerical solver for a solution of y, a sampling UQ approach would be to sample xi and solve for y as a function of it, then do that a number of times (this is referred to as Monte Carlo UQ). Then, calculate your statistics information to understand how your QoI reacts as a function of this uncertain parameter, and we can compare to an exact solution to understand how accurate our sampling approach is.

## Slide 19: Approach – Standard
    Run radiation transport simulation with particles
For i = 1:
    Sample
Stochastic parameter that influences output
    Calculate
Approximate variance over UQ space
Approximate mean over UQ space
Notes: Set parameters
For each UQ sample, sample xi and get sigT
Run RT solver for N_eta histories, tally response f
Calculate T-tilde by averaging all tallies for this sample
Calculate variance of tallies for this sample
Once repeated for all samples, avg MC noise over param space aka solver
Also calculate variance of T-tilde over param space aka total
Subtract solver from total for parametric variance in UQ space
*click* for each UQ sample, calculate sigmaT, then run mc simulations with N_eta number of histories, each of which has a tally response f.
Calculate the average transmittance for this UQ sample T-tilde, and the variance of the tally responses for this UQ sample
Once the loop over N_xi is complete, we can calculate the average sig_eta_sq over the entire UQ space, the variance of T-tildes over the UQ space, and then the parametric variance var T.

## Slide 20: Formulation – Variance deconvolution
Parameter uncertainty and MCRT uncertainty
Goal: from
Law of total variance
Notes: - From a UQ standpoint, goal is variance of QoI as a function of uncertain parameter
transmittance T = ratio
*click*
Uncertain param sigT, transmittance as function
*click*
Single code response func of xi
Also rep MC uncertainty mathematically, not a number, vector of RV
*click*
QoI is then expectation over eta,
*click* which must be estimated
Look at statistics, starting with expectation *click*
Expec of T over UQ space, aka first moment from Eq. 2, also approx.
What else do we care about?
So our goal is to obtain the variance of our quantity of interest over a number of UQ samples, and we can start by going through the statistics of our QoI. In this case, our quantity of interest will be transmittance, the ratio of particles that leave the system once they’ve entered. We have our uncertain parameter Sigma_t, and though you wouldn’t say the transport is a ‘function of’ the total cross section, here our quantity of interest transmittance becomes a function of the stochastic total cross section, as in Eq. 6 *click*
If our parameter uncertainty is xi, we can represent the monte carlo solver uncertainty using eta. Eta is not something sampled and plugged in, like xi is, but just mathematically represents the vector of random variables used to follow a particle along its ‘random walk’, and the resulting stochasticity. One UQ sample response would then actually then be the expectation over the entire eta space. We can bring back our first moment equation to find expectation, eq. 2, and this would be exact if we had an infinite number of samples. Instead, we have to settle for an approximation using a finite number ”samples” of our solver’s random behavior for one UQ sample, aka the number N_eta of histories we run per UQ sample. *click*
The first moment of the final code response, aka expectation of T, is also approximated using a finite number of UQ samples N_xi. Plugging Eq. 8 into Eq. 2 gives us Eq. 9, an approximation to the first moment of T using our code responses.

## Slide 21: Formulation – Variance Deconvolution
Apply law of total variance to
Goal: Parametric variance
Accessible: Total variance
Accessible: Average MCRT solver variance
Notes: - an intro to uncertainty quantification
In general, quantity of interest Q, a function of uncertain parameter xi
UQ propagates some source of uncertainty through a numerical code to evaluate statistics
Statistics one might be interested in, using the moment equation. Mean is first moment; variance
You can use a variety of strategies, surrogate and sampling and hybrid
sampling aka MC good for noisy QoI, example alg
In general you have some quantity of interest (or QoI) Q as a result of a numerical code. Uncertainty quantification is the process of propagating some sources of uncertainty through the numerical code to evaluate the statistics of your QoI. Q is then a function of you uncertainty parameter, xi
We have an example here of some statistics of your QoI you might be interested in, as functions of the moment equation. So eq. 1 is the order-p moment equation of Q. Eq 2 is the first moment of Q, aka the expectation or mean. The variance can be taken to be the second moment minus the square of the first moment. A simple example of a stochastic system might look mathematically is eq. 4, where you have some differential equation describing your system, and the parameter xi represents uncertainty in your system.
There are a variety of UQ strategies – surrogates, sampling-based methods, or hybrids of the two. In general, sampling methods (aka MC methods) are good for systems with noisy quantities of interest. Applied to eq. 4, If you have a numerical solver for a solution of y, a sampling UQ approach would be to sample xi and solve for y as a function of it, then do that a number of times (this is referred to as Monte Carlo UQ). Then, calculate your statistics information to understand how your QoI reacts as a function of this uncertain parameter, and we can compare to an exact solution to understand how accurate our sampling approach is.

## Slide 22: Approach – Variance Deconvolution Approach
For i = 1:
    Sample
    Run radiation transport simulation with particles
    Calculate
    Calculate
Stochastic parameter that influences output
Calculate average MCRT solver noise:
Calculate total variance:
Solve for parametric variance:
Now an MC/DC feature!
Notes: Set parameters
For each UQ sample, sample xi and get sigT
Run RT solver for N_eta histories, tally response f
Calculate T-tilde by averaging all tallies for this sample
Calculate variance of tallies for this sample
Once repeated for all samples, avg MC noise over param space aka solver
Also calculate variance of T-tilde over param space aka total
Subtract solver from total for parametric variance in UQ space
*click* for each UQ sample, calculate sigmaT, then run mc simulations with N_eta number of histories, each of which has a tally response f.
Calculate the average transmittance for this UQ sample T-tilde, and the variance of the tally responses for this UQ sample
Once the loop over N_xi is complete, we can calculate the average sig_eta_sq over the entire UQ space, the variance of T-tildes over the UQ space, and then the parametric variance var T.

## Slide 23: Formulation – Estimator evaluation
True or continuous value is approximated using an estimator .
An estimator can be characterized by its mean-squared error (MSE), which captures both its variance and bias.
  Variance characterizes how far the estimator is, on average, from its mean.
  Bias characterizes how far the estimator’s mean is, on average, from the true value.

## Slide 24: Results – Analytic problem
Mat 1 | 
Mat 2 | 
Mat 3 | 
Mat 1 | 
Mat 2 | 
Mat 3 | 
Attenuation through 1D slab, 3 materials
Uncertain total cross sections
: Transmittance, percent of particles that exit
Analytic solution for

## Slide 25: Results – Analytic problem
Variances of estimators
Bias of estimating
Distribution of results over 25000 repetitions
= Estimator value
= (Known) true value
Notes: Table on the left shows the results for transmittance and parametric variance for a benchmark (overresolved) configuration, just one repetition (which is a sample), and the analytic results.
Repeated algorithm 25,000 times to get statistics of estimate of varT and varTtilde
300 Nxi 5 Neta
Clustered around analytic solution, estimators are unbiased
Strong indication that we get a good estimate of our variances
For a sample problem with 300 UQ samples and 5 particles per sample with 25,000 repetitions. Clustered around analytic solution, bc estimators are unbiased.

## Slide 26: Example Problem – Visualize Motivations
Increased drives bias down
Notes: Table on the left shows the results for transmittance and parametric variance for a benchmark (overresolved) configuration, just one repetition (which is a sample), and the analytic results.
Repeated algorithm 25,000 times to get statistics of estimate of varT and varTtilde
300 Nxi 5 Neta
Clustered around analytic solution, estimators are unbiased
Strong indication that we get a good estimate of our variances
For a sample problem with 300 UQ samples and 5 particles per sample with 25,000 repetitions. Clustered around analytic solution, bc estimators are unbiased.

## Slide 27: Infinite Slab Lattice Problem
1-cm thick slabs
Reflecting BCs
Data from C5G7 benchmark
Fast (1.36 – 10 MeV) neutron source at the center of water
Goal: variance of to
  80% variance in water and crtl. rod. capture and scatter xsec
Fast neutron flux
(9.2 keV – 10 MeV)
Slow neutron flux
(< 9.2 keV)

## Slide 28: What is without UQ?
Brute force: as
MCNP calls this R (rel. error)
With no UQ, no batches:
UQ: divided between and

## Slide 29: Infinite Slab Lattice Problem
Reference solution , ,
Var-D and brute force , ,
QoI: Cell-avg
Var-D consistently out-performs brute force
QoI: Cell-avg

## Slide 30: Error and Figure of Merit
Figure of Merit
  Reference solution:
: Runtime
: rel. error (2-norm)
Constant
Increasing decreasing
Run without MPI (i.e., serially)
FOM
Var-D shows efficiency tradeoff between N_particle and N_batch
Relative error

## Slide 31: Formulation – Cost analysis
For given cost, find such that
Variance of a sample estimator:
Independent variable
Sample estimator:

## Slide 32: Results – Cost analysis
as a function of for a variety of total estimator costs, log-log plot. Unfilled point is minimum .
Total estimator cost
Notes: Repeated algorithm 25,000 times to get statistics of estimate of varT and varTtilde
300 Nxi 5 Neta
Clustered around analytic solution, estimators are unbiased
Strong indication that we get a good estimate of our variances
Poster compares to previously developed method
Other work includes varying Nxi and Neta, adding in scattering problem
For a sample problem with 300 UQ samples and 5 particles per sample with 25,000 repetitions. Clustered around analytic solution, bc estimators are unbiased. Poster does comparison w/ other method

## Slide 33: Results – UQ cost analysis
as a function of for a variety of total estimator costs, log-log plot. Unfilled point is minimum .
Total estimator cost
Notes: Repeated algorithm 25,000 times to get statistics of estimate of varT and varTtilde
300 Nxi 5 Neta
Clustered around analytic solution, estimators are unbiased
Strong indication that we get a good estimate of our variances
Poster compares to previously developed method
Other work includes varying Nxi and Neta, adding in scattering problem
For a sample problem with 300 UQ samples and 5 particles per sample with 25,000 repetitions. Clustered around analytic solution, bc estimators are unbiased. Poster does comparison w/ other method

## Slide 34: Results – UQ cost analysis
Analytically calculate all terms in equation
scipy.optimize.brentq() finds 0 of function on a given interval using Brent’s method
Analytically calculate all terms in equation
Goal: pilot study to numerically calculate needed terms
as a function of for a variety of total estimator costs, log-log plot.
Notes: Estimator is unbiased, ie we converge to the mean with no biasing error introduced
For a given total estimator cost, like 2000 total histories, there’s various combinations of Nxi and Neta possible
Goal: minimized variance of S^2, aka deviation from mean

## Slide 35: Discussion
Variance deconvolution is an effective tool for computing parametric variance with stochastic solvers.
There is an optimal distribution of computational cost between parameter samples and solver samples.
The optimal distribution of computational cost is problem-dependent and requires higher-order moments of the QoI to estimate.

## Slide 36: Background – sensitivity indices (SI)
Fractional contribution of
not
Consider and
General case
Total sensitivity index (SI)
Fractional contribution of and all of its interactions
First-order sensitivity index (SI)
not
Notes: https://arxiv.org/ftp/arxiv/papers/2203/2203.00639.pdf
S_i =
“Fractional reduction in V[Q] which would be obtained on average if xi_i could be fixed.”
“Fraction of variance that would remain on average if one received perfect information on all other factors”

## Slide 37: Formulation – Sensitivity indices
QoI is a function of uncertain input parameters,
Consider dividing the set into one parameter and the subset of the remaining parameters
not
Contribution of
Total sensitivity index (SI)
Contribution of and its interactions with all
First-order sensitivity index (SI)

## Slide 38: Standard Approach – Sampling-based Saltelli method
Given , generate a matrix of independent input samples and define matrices and , each containing half of the sample
For all inputs, create matrix using all columns of except the th column, which is from
Compute model output vector of dimension for , , and all

## Slide 39: Standard Approach – Sampling-based Saltelli method
Given , generate a matrix of independent input samples and define matrices and , each containing half of the sample
For all inputs, create matrix using all columns of except the th column, which is from
Compute model output vector of dimension for , , and all
Estimate full set of first- and total- order SIs using sampling estimators

## Slide 40: Standard Approach – Sampling-based Saltelli method
Estimate full set of first- and total- order SIs using sampling estimators
Different sampling estimators have slightly different properties.

## Slide 41: Standard Approach – With stochastic solvers
Estimate full set of first- and total- order SIs using sampling estimators
Different sampling estimators have slightly different properties.

## Slide 42: Formulation – Sensitivity indices with variance deconvolution
Consider effect of on
How does this compare to and ?

## Slide 43: Formulation – Sensitivity indices with variance deconvolution
and approximate and
How can we estimate and from ?

## Slide 44: Saltelli Approach – With variance deconvolution
Estimate full set of first- and total- order SIs using sampling estimators
How do and compare as estimators for ?

## Slide 45: Results – Ishigami function
Known function with analytic solutions commonly used to evaluate GSA methods
Add stochastic parameter multiplied by a constant
Known:

## Slide 46: Results – Ishigami function
Estimator statistics over 200 repetitions

## Slide 47: Results – Ishigami function
Estimator statistics over 200 repetitions

## Slide 48: Results – Ishigami function
Estimator statistics over 200 repetitions

## Slide 49: Results – Ishigami function
Estimator statistics over 200 repetitions

## Slide 50: Results – Ishigami function
Estimator statistics over 200 repetitions

## Slide 51: Results – Ishigami function
Estimator statistics over 200 repetitions

## Slide 52: Results – Slab
1D slab with three material regions
Neutral particle, steady-state, mono-energetic, attenuation-only
Problem definition
Cosine of beam-source incidence angle
Uncertain parameter groups
Material region boundary locations
Total cross sections
Comparison
Straightforward Saltelli method vs. variance deconvolution modification
Number of MC RT particle histories: vs.
Benchmark: , analytic optical thickness Test:
range
range

## Slide 53: Distributions over 25000 repetitions
First-order SI for cosine of beam incident angle

## Slide 54: Distributions over 25000 repetitions
Total SI for cosine of beam incident angle

## Slide 55: Distributions over 25000 repetitions
First-order SI for total cross section

## Slide 56: Distributions over 25000 repetitions

## Slide 57: Results over 25000 repetitions
Saltelli method vs. Saltelli modified with variance deconvolution (Saltelli-VarD)
 | Benchmark | Saltelli |  | Saltelli-VarD | 
 | 0.6752(2) | 0.27(8) | 0.66(8) | 0.67(8) | 0.67(2)
 | Benchmark | Saltelli |  | Saltelli-VarD | 
 | 0.6752(2) | 0.27(8) | 0.66(8) | 0.67(8) | 0.67(2)

## Slide 58: Discussion
Variance deconvolution modification to Saltelli method yields accurate results for GSA indices.
Variance deconvolution estimator behavior is dependent on the statistical properties of the existing estimator.
The variance deconvolution estimator is unbiased, but its variance can be appreciably larger than the standard estimator.

## Slide 59: The C5G7-3D Benchmark
7-energy group, 3-dimensional, light water reactor core with 4 fuel types
  Fuel modeled as homogenized pin surrounded by water moderator
8 uncertain input parameters, each normally distributed with 5% standard deviation
  Densities of all fuel types
  Radii of all fuel pins
2 quantities of interest
  Core k-eigenvalue
  Pin-wise core fission rate distribution
Modeled using Monte Carlo Dynamic Code (MC/DC)
Reflected boundary
Reflected boundary
Vacuum boundary
Vacuum boundary
Pin Cell
2D Southeast quadrant of reactor core. Reactor has quarter-core symmetry.

## Slide 60: C5G7 Results I – Uncertainty of keff
Refence keff
  50 inactive cycles, 100 active cycles, histories/cycle
Characterize

## Slide 61: C5G7 Results I – Sensitivity indices of keff
Parameter | 
Radius – UO2 | 0.8043
Radius – MOX7.0% | 0.1178
Radius – MOX8.7% | 0.1028
Radius – MOX4.5% | 0.0851
Density – UO2 | 0.0699
Density – MOX7.0% | 0.0647
Density – MOX8.7% | 0.0633
Density – MOX4.5% | 0.0614
SUM | 1.3693
Parameter | 
Radius – UO2 | 0.8043
Radius – MOX7.0% | 0.1178
Radius – MOX8.7% | 0.1028
Radius – MOX4.5% | 0.0851
Density – UO2 | 0.0699
Density – MOX7.0% | 0.0647
Density – MOX8.7% | 0.0633
Density – MOX4.5% | 0.0614
SUM | 1.3693
Parameter | 
Radius – UO2 | 0.7936
Radius – MOX7.0% | 0.0680
Radius – MOX8.7% | 0.0524
Radius – MOX4.5% | 0.0334
Density – UO2 | 0.0176
Density – MOX4.5% | 0.0119
Density – MOX7.0% | 0.0106
Density – MOX8.7% | 0.0085
SUM | 0.9960
Parameter | 
Radius – UO2 | 0.7936
Radius – MOX7.0% | 0.0680
Radius – MOX8.7% | 0.0524
Radius – MOX4.5% | 0.0334
Density – UO2 | 0.0176
Density – MOX4.5% | 0.0119
Density – MOX7.0% | 0.0106
Density – MOX8.7% | 0.0085
SUM | 0.9960
Indicates small interaction effects
Indicates large interaction effects
Radii
Densities

## Slide 62: C5G7 Results I – Sensitivity indices of keff
Parameter | 
Radius – UO2 | 0.7936
Radius – MOX7.0% | 0.0680
Radius – MOX8.7% | 0.0524
Radius – MOX4.5% | 0.0334
Density – UO2 | 0.0176
Density – MOX4.5% | 0.0119
Density – MOX7.0% | 0.0106
Density – MOX8.7% | 0.0085
SUM | 0.9960
Parameter | 
Radius – UO2 | 0.7936
Radius – MOX7.0% | 0.0680
Radius – MOX8.7% | 0.0524
Radius – MOX4.5% | 0.0334
Density – UO2 | 0.0176
Density – MOX4.5% | 0.0119
Density – MOX7.0% | 0.0106
Density – MOX8.7% | 0.0085
SUM | 0.9960
Parameter | 
Radius – UO2 | 0.8043
Radius – MOX7.0% | 0.1178
Radius – MOX8.7% | 0.1028
Radius – MOX4.5% | 0.0851
Density – UO2 | 0.0699
Density – MOX7.0% | 0.0647
Density – MOX8.7% | 0.0633
Density – MOX4.5% | 0.0614
SUM | 1.3693
Parameter | 
Radius – UO2 | 0.8043
Radius – MOX7.0% | 0.1178
Radius – MOX8.7% | 0.1028
Radius – MOX4.5% | 0.0851
Density – UO2 | 0.0699
Density – MOX7.0% | 0.0647
Density – MOX8.7% | 0.0633
Density – MOX4.5% | 0.0614
SUM | 1.3693

## Slide 63: C5G7 Results III – Uncertainty of fission rate distribution
Pin-wise core fission rate distribution at plane
Ability to explore entire parameter space and entire phase space
Relative fission distribution
Relative parametric uncertainty %

## Slide 64: Discussion
Variance deconvolution estimates variances and sensitivity indices for 50X lower computational cost than standard approach
Hypotheses on large vs. small interaction effect discrepancy:
  Correlation effects between keff cycles – do we see the effect increase if we increase correlation?
  Estimator allows for – do estimators that uphold show this effect?

## Slide 65: In Conclusion…
Variance deconvolution is a novel approach for sampling-based UQ and GSA.
I have analyzed and compared the statistical properties of the developed estimators and those of a standard approach.
Variance deconvolution was shown to be accurate with analytical test cases and was tested with various physics models and quantities of interest.
Variance deconvolution has been shown theoretically and numerically to be more computationally efficient than a standard sampling approach for UQ and for many cases for GSA.
I implemented variance deconvolution in multiple Monte Carlo radiation transport codebases and developed a stand-alone python module for wrapper functionality around existing stochastic computational codes.
I, along with colleagues, published and presented on this work in journals and conferences relevant for computational mathematics and nuclear science and engineering.

## Slide 66: Full list of publications related to this work
K.B. Clements, T.S. Palmer, and I. Variansyah, “Monte Carlo Sensitivity Analysis for the C5G7 Benchmark,” Accepted with minor revisions to The International Conference on Mathematics and Computational Methods Applied to Nuclear Science and Engineering (M&C), Apr. 2025, Denver, CO.
K.B. Clements and T.S. Palmer, “Sampling-based sensitivity indices for stochastic solvers with application to Monte Carlo radiation transport,” Draft for submission to Journal of Computational Physics.
K.B. Clements, G. Geraci, A.J. Olson, and T.S. Palmer, “A Variance Deconvolution Estimator for Efficient Uncertainty Quantification in Monte Carlo Radiation Transport Applications,” Journal of Quantitative Spectroscopy and Radiative Transfer, Jun. 2024, doi: 10.1016/j.jqsrt.2024.108958.
J.P. Morgan et al., “Journal of Open Source Software: Monte Carlo / Dynamic Code (MC/DC): An accelerated Python package for fully transient neutron transport and rapid methods development,” Journal of Open Source Software, Mar. 2024, [Online]. Available: https://joss.theoj.org/papers/2974750fe1da49e79bc155f1171263d9
K.B. Clements, G. Geraci, A.J. Olson, and T.S. Palmer, “Global sensitivity analysis in Monte Carlo radiation transport’’, in The International Conference on Mathematics and Computational Methods Applied to Nuclear Science and Engineering (M&C), Aug. 2023, Niagara Falls, Canada.
A.J. Olson, K.B. Clements, and J.M. Petticrew, “A sampling-based approach to solve Sobol' indices using variance deconvolution for arbitrary uncertainty distributions’’, in Transactions of the American Nuclear Society, Nov. 2022, pp. 450-453. doi: 10.13182/T127-39783.
K.B. Clements, G. Geraci, and A.J. Olson, "Numerical investigation on the performance of a variance deconvolution estimator’’ in Transactions of the American Nuclear Society, Jun. 2022, pp. 344-347. doi: 10.13182/T126-38365.

## Slide 67: Opportunities for future work
Analyzing correlated input parameters, particularly nuclear data uncertainty.
Computational cost optimization, including development of a feasible pilot-study approach that could find the optimal balance between parameter realizations and solver realizations.
UQ and GSA for time-dependent radiation transport problems, which could see similar correlation effects to the keff problem.
Runtime comparison of parallelization over parameter evaluations vs over particle histories in Monte Carlo Dynamic Code.

## Slide 68: Acknowledgements and Logos
The Center for Exascale Monte Carlo Neutron Transport (CEMeNT)
High performance computing resources and support
Continued internship and support
This work was supported by the Center for Exascale Monte-Carlo Neutron Transport (CEMeNT), a PSAAP-III project funded by the Department of Energy, grant number DE-NA003967.
Sandia National Laboratories is a multimission laboratory managed and operated by National Technology & Engineering Solutions of Sandia, LLC, a wholly owned subsidiary of Honeywell International Inc., for the U.S. Department of Energy’s National Nuclear Security Administration under contract DE-NA0003525.

## Slide 69: More acknowledgements
The committee
Dr. Todd Palmer
Dr. Kyle Niemeyer
Dr. Izabela Gutowska
Dr. Tianyi Chen
Dr. Mike Bailey
The Radiation Transport and Reactor Physics research group, past and present

## Slide 70: Implementation in MC/DC

## Slide 71: Additional estimators for SIs